## Slide 1: Roadmap
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches

## Slide 2: Ethernet
“dominant” wired LAN technology:
first widely used LAN technology
simpler, cheap
kept up with speed race: 10 Mbps – 400 Gbps
single chip, multiple speeds (e.g., Broadcom BCM5761)
Metcalfe’s Ethernet sketch
“主导”有线局域网技术:
首先广泛使用的局域网技术
更简单、便宜
跟上速度竞赛:10mbps - 400gbps
单芯片，多种速度

## Slide 3: Ethernet: physical topology
bus: popular through mid 90s
  all nodes in same collision domain (can collide with each other)
bus: coaxial cable
switched
switched: prevails today
  switch-based star topoloy
  active link-layer 2 switch in center
  each “spoke” runs a (separate) Ethernet protocol (nodes do not collide with each other)
Star topology
同轴电缆
总线:流行于90年代中期．
同一碰撞域中的所有节点(可以相互碰撞)
交换机:今天流行．
星形拓扑．
链路层交换机
在中心每个“辐条”运行一个(单独的)以太网协议(节点之间不碰撞)

## Slide 4: Ethernet frame structure
sending interface encapsulates IP datagram (or other network layer protocol packet) in Ethernet frame
dest.
address
source
address
data (payload)
CRC
preamble
type
preamble:
used to synchronize receiver, sender clock rates
7 bytes of 10101010 followed by one byte of 10101011
前同步码
用于同步接收方、发送方的时钟速率
8个字节：10101010*7+10101011

## Slide 5: Ethernet frame structure (more)
dest.
address
source
address
data (payload)
CRC
preamble
type
addresses: 6 byte source, destination MAC addresses
  if adapter receives frame with matching destination address, or with broadcast address (e.g., ARP packet), it passes data in frame to network layer protocol
  otherwise, adapter discards frame
type: indicates higher layer protocol
  mostly IP but others possible, e.g., Novell IPX, AppleTalk
  used to demultiplex up at receiver
CRC: cyclic redundancy check at receiver
  error detected: frame is dropped
地址：源、目的mac地址 6字节
如果适配器接收到目的地址匹配的帧，或者广播地址，它将帧中的数据传递给网络层协议，否则，适配器丢弃帧
类型:表示上层协议
主要是IP，但也有可能是其他的，
用于在接收器上进行多路复用
循环冗余检测
错误检测

## Slide 6: 802.3 Ethernet standards: link & physical layers
  different physical layer media: fiber, cable
application
transport
network
link
physical
MAC protocol
and frame format
100BASE-TX
100BASE-T4
100BASE-FX
100BASE-T2
100BASE-SX
100BASE-BX
fiber physical layer
copper (twister pair) physical layer
many different Ethernet standards
  common MAC protocol and frame format
  different speeds: 2 Mbps, 10 Mbps, 100 Mbps, 1Gbps, 10 Gbps, 40 Gbps
不同的以太网标准
相同的mac协议和帧格式
不同速度
不同媒介

## Slide 7: Roadmap
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches

## Slide 8: Ethernet switch
Switch is a link-layer device:
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links
transparent: hosts unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured
Switch是链路层设备:
存储，转发以太网帧
检查传入帧的MAC地址，有选择地将帧转发到一个或多个传出链接
透明:主机不知道交换机的存在
即插即用，自我学习
交换机无需配置

## Slide 9: Switch forwarding table
A
A’
B
B’
C
C’
1
2
3
4
5
6
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  Switches have the self-learning property.
每个交换机都有交换表
主机mac地址，接口编号，时间戳
通过自我学习创建和维持交换表

## Slide 10: Switch: self-learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60
  when a frame received on an interface, switch “learns” 1) the MAC address in the frame’s source address field, 2) the interface from which the frame arrived, and 3) the current time.
  records sender/incoming LAN segment pair in switch table
收到帧时记录

## Slide 11: Interconnecting switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 12: Thank You!