## Slide 1: Packet delay - Solution
Q: How long does it take a packet of length 1,000 bytes to propagate over a link of distance 2,500 km, propagation speed 2.5*10^8 m/s, and transmission rate 2 Mbps?
Hint: some irrelevant information is provided in the problem to mislead you.
Propagation delay: 2500 * 10^3 / (2.5 * 10^8) = 0.01 seconds = 10 ms
Q: More generally, how long does it take a packet of length L (bits) to propagate over a link of distance d (meter), propagation speed s (m/s), and transmission rate R bps?
Hint: be careful with the units.
Propagation delay: d/s seconds
Q: Does this delay depend on packet length?
  No
  Q: Does this delay depend on transmission rate?
  No

## Slide 2: Caravan analogy
cars “propagate” at 100 km/hr
toll booth takes 12 sec to service a car (bit transmission time)
car ~ bit; caravan ~ packet
entire caravan stored and forwarded
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll booth: 100km/(100km/hr) = 1 hr
A: 62 minutes
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km

## Slide 3: Caravan analogy
toll booth
toll booth
(aka router)
ten-car caravan
(aka 10-bit packet)
100 km
100 km
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
A: Yes! after 7 min, first car arrives at second booth; three cars are still at first booth
First car spends 1 minute at toll booth, 6 minutes propagating through the link, then arrives at second booth
At this point, car 8 is still at the first toll booth (with 2 cars waiting behind)

## Slide 4: End-to-end delay
Definition: end-to-end delay is the total of all nodal delay from source to destination
  Include a sequence of intermediate nodes on the way to the destination
Varies over time as the sources of delay increase and decrease
Delay components: transmission delay dtrans, propagation delay dprop, processing delay dproc and queuing delay dqueue
Round-trip time (RTT): end-to-end delay measured in both directions
  from source to destination and then back again
  Doesn’t necessarily have to be the same path/route

## Slide 5: End-to-end delay - Quiz
Assume the length of a packet is 16000 bits.
The speed of propagation on each link is 3x10^8 m/sec
Round your answer to two decimals after leading zeros
Q: Can you compute the end-to-end delay from source to destination taking into account transmission delay and propagation delay?
Hint: separately calculate the delay for each link and then get the summation

## Slide 6: End-to-end delay - Solution
Link 1 total delay = dtrans + dprop = 16000 bits / 10 Mbps + 1000 m / (3*10^8 m/s) = 1.6 ms
Link 2 total delay = dtrans + dprop = 16000 bits / 10 Mbps + 1000 * 10^3 m / (3*10^8 m/s) = 4.9 ms
Link 3 total delay = dtrans + dprop = 16000 bits / 1000 Mbps + 1000 m / (3*10^8 m/s) = 0.0193 ms
The total delay = Link 1 total delay + Link 2 total delay + Link 3 total delay
= 1.6 ms + 4.9 ms + 0.0193 ms = 6.5 ms
propagation delay negligible

## Slide 7: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to routers along the route to a destination
For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live (TTL) field value of i)
  router i will return packets to sender
  sender can reconstruct the route taken by packets flowing from source to destination and determine the round-trip delays to all the intervening routers

## Slide 8: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic link
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu
Notes: First column: the number of the routers along the path
Second column: name of router
Third column: address of the router
Last three columns: round-trip delays for three packets/probes
The total packets sent to test are 19 * 3 packets.

## Slide 9: Real Internet delays and routes
Traceroute command
For Windows: tracert
For Mac OS: traceroute
The detailed instructions on how to use traceroute commands can be found in the uploaded tutorial in the Tutorials section on Moodle.

## Slide 10: Packet loss overview
Packets Loss occurs when a node drops or discards a packet
This means that the packet does not reach its destination
Packet Loss reduces the useable throughput of a device, as the number of useful bits sent is less
For reliable protocols, packet loss will cause retransmission to occur
  There will also be a period of time where we wait to see if the packet does arrive
  Once this expires, and no packet has arrived, a retransmission request is sent
  This introduces additional latency, as the packet has to make the full journey again, regardless of where it was lost

## Slide 11: Queuing delay and packet loss
Packet Loss has a close relationship with Queuing Delay
When packets arrive at a rate greater than the maximum supported throughput, the device queue starts to fill
Newly arriving packets wait in the buffer before transmission
A
B
packet being transmitted
buffer (waiting area)

## Slide 12: Queuing delay and packet loss
* Check out the Java applet for an interactive animation on queuing and loss (https://media.pearsoncmg.com/aw/ecs_kurose_compnetwork_7/cw/content/interactiveanimations/queuing-loss-applet/index.html)
When the buffer is full, additional packets cannot be received
  As a result, they are discarded and lost
Lost packets may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
buffer(waiting area)
packets arriving to full buffer is
dropped (loss)

## Slide 13: Queuing delay and packet loss
R: transmission rate (bps)
L: packet length (bits)
a: average packet arrival rate (packets/sec)
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than that can be serviced - average delay infinite (if queue has infinite capacity)! In practice, packet loss happens since the queue capacity is finite.
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
* Check out the Java applet for an interactive animation on queuing and loss (https://media.pearsoncmg.com/aw/ecs_kurose_compnetwork_7/cw/content/interactiveanimations/queuing-loss-applet/index.html)

## Slide 14
When dropping packets because of a full queue, we have control over which packet to drop
In the examples we have discussed, we assumed that the newly arriving packet is dropped if the queue is full
  called Tail Drop policy
However, other techniques can be used:
  Random Drop: Drop any packet within the queue
  Quality-of-Service (QoS) Aware: Packets will be dropped given their priority; provide fairness and guarantee throughput for sensitive services, such as voice calls or live video
Queuing Disciplines

## Slide 15
Packets can also be lost in the physical medium, particularly with unguided radio technologies
Hardware and software in devices can also fail
  This includes errors and corruption
  It may still be sent, but fail to pass a checksum verification
Devices can also be attacked
  A simple way to introduce loss would be to bombard a device with packets, and fill up it’s buffers
  This prevents other users from sending packets, either completely or at a reduce rate
  “Denial of Service”
Other Sources of Loss

## Slide 16
Works in a similar fashion to traceroute
Creates packets to be sent out to the target hosts (rather than those on the path)
Measures round-trip time (RTT) (as with traceroute)
Also includes a measurement of packet loss by keeping track of how many messages were sent, and how many responses were received
Has the advantage that it can repeatedly measure this over many packets
The detailed instructions on how to use ping commands on Windows and Mac OS can be found in the uploaded tutorial in the Tutorials section on Moodle.
Measuring Loss - ping