## Slide 1: Throughput
throughput: transmission rate (bits/sec) at which bits are being sent from sender to receiver
  instantaneous: rate at any instant of time
  average: average rate over longer period of time
  peak: highest rate so far
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)
client

## Slide 2: Throughput
Rs < Rc What is average end-to-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-to-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec
min(Rc , Rs)
Rc
Rs

## Slide 3: Throughput - Quiz
Suppose Host A wants to send a large file to Host B. The path from Host A to Host B has three links of rates R1 = 500 kbps, R2 = 2 Mbps, and R3 = 1 Mbps.
Q: Assuming no other traffic in the network, what is the average throughput for the file transfer from Host A to Host B?
Q: Suppose the file is 4 * 10^6 bytes. Dividing the file size by the throughput, roughly how long will it take to transfer the file to Host B?
Hint: 1 byte = 8 bits
Q: Repeat the above two questions, but now with R2 reduced to 100 kbps.

## Slide 4: Throughput - Solution
Suppose Host A wants to send a large file to Host B. The path from Host A to Host B has three links of rates R1 = 500 kbps, R2 = 2 Mbps, and R3 = 1 Mbps.
Q: Assuming no other traffic in the network, what is the average throughput for the file transfer from Host A to Host B?
min(R1, R2, R3) = 500 kbps
Q: Suppose the file is 4 * 10^6 bytes. Dividing the file size by the throughput, roughly how long will it take to transfer the file to Host B?
Hint: 1 byte = 8 bits
Transmission delay = 8 * 4 * 10^6 /(500 * 10^3) = 64 s
Q: Repeat the above two questions, but now with R2 reduced to 100 kbps.
min(R1, R2, R3) = 100 kbps
Transmission delay = 8 * 4 * 10^6 /(100 * 10^3) = 320 s

## Slide 5: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-to-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 6: Throughput: network scenario - Quiz
Q：
What is the maximum achievable end-end throughput (in Mbps) for each of four client-to-server pairs, assuming that the middle link is fairly shared (divides its transmission rate equally)?
Which link is the bottleneck link? Format as Rc, Rs, or R.
Assuming that the servers are sending at the maximum rate possible, what are the link utilizations for the server links (RS), for the client links (Rc), and for the shared link (R), respectively?

## Slide 7: Throughput: network scenario - Solution
The maximum achievable end-end throughput is the capacity of the link with the minimum capacity, which is 20 Mbps
The bottleneck link is the link with the smallest capacity between RS, RC, and R/4. The bottleneck link is Rc.
The server's utilization = Rbottleneck / RS = 20 / 70 = 0.29.
The client's utilization = Rbottleneck / RC = 20 / 20 = 1.
The shared link's utilization = Rbottleneck / (R / 4) = 20 / (200 / 4) = 0.4.

## Slide 8: Week 2: roadmap
Performance: loss, delay, throughput
Protocol layers, service models

## Slide 9: Protocol “layers” and reference models
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question:
is there any hope of organizing a network architecture?
…. or at least our discussion of networks?

## Slide 10: Example: send letter to friend
Send letter to friend

## Slide 11: Example: send letter to friend clear separation of concerns
Writes letter
Reads Letter
Takes letter from sender to post office
Takes letter from post office to recipient
Decides how the letter will be routed to destination
Transports the letter
Doesn’t know how the postal network works
Doesn’t know how the letter will be routed
Doesn’t know the contents of the letter
Doesn’t know the sender or recipient

## Slide 12: Example: send letter to friend Abstraction leads to layering through decomposition
Writes letter
Reads Letter
Takes letter from sender to post office
Takes letter from post office to recipient
Decides how the letter will be routed to destination
Transports the letter
layers: each layer implements a service by
  performing certain actions within that layer
  relying on services provided by layer below

## Slide 13: Why layering?
dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system (black box)
  e.g., change in postman procedure doesn’t affect rest of system
layering in other complex systems?