## Slide 1: CNSCC.203 Computer Networks Transport Layer
Muhammad Azhar Iqbal
azhar.iqbal@lancaster.ac.uk
Credit goes to Dr. Matt Broadbent, Dr. Vasileios Giotsas, and Dr. Wenjuan Yu at SCC for designing module SCC.203.

## Slide 2: Transport Layer I: roadmap
Transport Layer Overview
  Transport Layer services & functions
  Internet Transport Layer
Multiplexing/ De-multiplexing
  Connectionless & connection-oriented
User Datagram Protocol – UDP
  UDP features
UDP Checksum
  Checksum calculation

## Slide 3: Transport services and protocols
provide logical communication between application processes running on different hosts
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
transport protocols implemented in end systems not in routers:
  sender: breaks application messages into segments, passes to network layer
  receiver: reassembles segments into messages, passes to application layer
two transport protocols available to Internet applications
  TCP, UDP
在不同主机上运行的应用程序进程之间提供逻辑通信
Notes: By logical communication , we mean that from an application’s perspective, it is as if the hosts running the processes
were directly connected; in reality, the hosts may be on opposite sides of the
planet, connected via numerous routers and a wide range of link types.

## Slide 4: Transport Layer Service
Service Types
Connection oriented service
    3 phases: connection set-up, data transfer, disconnect
Connectionless service
    Transfer of isolated units
Task
To isolate upper layers from technology, design and imperfections of subnet
Creates major boundary between provider and user of (reliable) data transmission service
Aim
To Improve the Network Service quality that users and layers want to get from the network layer, e.g.: Reliable service, Necessary time guarantees
Implementation: transport entity
    Software and/or hardware?
    Software part usually contained within the kernel (process, library)
面向连接的服务
3个阶段:连接建立，数据传输，断开
无连接服务
转移隔离单位
将上层与子网的技术、设计和缺陷隔离开来
在(可靠)数据传输服务的提供者和用户之间建立主要的界限
提高用户和各层希望从网络层获得的网络服务质量
如:可靠的服务，必要的时间保证
Notes: Usually the transport layer is implemented in software (typically by the operating system or microcontroller firmware). Some TCP offload hardware does exist, but on modern CPUs the benefits are limited (and there are major drawbacks, principally the loss of direct control over the function of the transport layer). For UDP there isn't really any point as the transport layer doesn't add very much overhead.

## Slide 5: Internet Transport Layer
Lowest level end-to-end protocol
Header generated by sender is interpreted only by destination; routers / gateways view transport header as part of the payload
Can add extra functionality to the best effort packet delivery service provided by IP
Can make up for shortcomings of core network
最低级别端到端协议
能弥补核心网的不足

## Slide 6: Transport vs. network layer services and protocols
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
household analogy:
12 kids in Ann’s house sending letters to 12 kids in Bill’s house:
hosts = houses
processes = kids
app messages = letters in envelopes
transport protocol = Ann and Bill who mux/demux to in-house siblings
network-layer protocol = postal service

## Slide 7: Two principal transport-layer protocols
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
logical end-end transport
TCP: Transmission Control Protocol
  reliable, in-order delivery
  congestion control
  flow control
  connection setup
UDP: User Datagram Protocol
  unreliable, unordered delivery
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
可靠，按顺序交付
拥塞控制
流控制
连接设置
不可靠的、无序的交付
无装饰的“尽最大努力”IP的扩展
延迟保证
带宽保证

## Slide 8: Some Transport Layer Functions
Multiplexing/de-multiplexing data for multiple applications
Uses “port’’ abstraction
Connection establishment
Logical end-to-end connection
Error control
Hides unreliability of network layer from applications
  Corruption, loss, duplication, reordering
End-to-end flow control
To avoid flooding the receiver
Congestion control
To avoid flooding the network
拥塞控制
避免网络泛滥
端到端流量控制
避免淹没接收器
错误控制
对应用程序隐藏网络层的不可靠性腐败，损失，复制，重组

## Slide 9: Transport Layer I: roadmap
Transport Layer Overview
  Transport Layer services & functions
  Internet Transport Layer
Multiplexing/ De-multiplexing
  Connectionless & connection-oriented
User Datagram Protocol – UDP
  UDP features
UDP Checksum
  Checksum calculation

## Slide 10: Multiplexing/demultiplexing
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
handle data from multiple
sockets, add transport header (later used for demultiplexing)
and pass segments to network layer
multiplexing at sender:
多路复用在发送方:
处理来自多个套接字的数据，添加传输头(稍后用于多路分离)并将段传递到网络层
在接收方多路分解:
使用头信息将收到的段发送到正确的套接字

## Slide 11: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format
主机接收IP数据报
每个数据报都有源IP地址、目的IP地址
每个数据报携带一个传输层段
每个段都有源端口号，目的端口号

## Slide 12: Connectionless demultiplexing
Recall:
when creating socket, must specify host-local port #:
DatagramSocket mySocket1 = new DatagramSocket(12534);
when receiving host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP/UDP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at receiving host
无连接多路分解
使用UDP
由目的IP和port对应socket,与源IP和port无关

## Slide 13: Connectionless demultiplexing: an example
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?
Host A
Host B

## Slide 14: Connection-oriented demultiplexing
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
server may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
  each socket associated with a different connecting client
demux: receiver uses all four values (4-tuple) to direct segment to appropriate socket
面向连接多路分解
使用TCP
每一个元组（由四个标识符区别）对应一个socket

## Slide 15: Connection-oriented demultiplexing: example
transport
application
physical
link
network
P1
transport
application
physical
link
P4
transport
application
physical
link
network
P2
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
server: IP address B
Three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets