## Slide 1: Transport Layer I: roadmap
Transport Layer Overview
  Transport Layer services & functions
  Internet Transport Layer
Multiplexing/ De-multiplexing
  Connectionless & connection-oriented
User Datagram Protocol – UDP
  UDP features
UDP Checksum
  Checksum calculation

## Slide 2: UDP: User Datagram Protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
no connection establishment (which can add RTT delay)
simple: no connection state at sender, receiver
small header size
no congestion control
  UDP can blast away as fast as desired!
  can function in the face of congestion
Why is there a UDP?
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
UDP is “mostly IP with a short transport header”
  Source and destination port
  Ports allow for dispatching of messages to receiver process
没有连接建立
没有连接状态
头部小
没有拥塞控制

## Slide 3: UDP: User Datagram Protocol [RFC 768]
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP
if reliable transfer needed over UDP (e.g., HTTP/3):
  add needed reliability at application layer
  add congestion control at application layer
承载网络管理数据
可在应用层添加可靠数据传输、拥塞控制
Notes: HTTP/3 uses QUIC, a protocol developed initially by Google where user space congestion control is used over UDP.

## Slide 4: UDP segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including UDP header and UDP data
data to/from application layer

## Slide 5: Transport Layer I: roadmap
Transport Layer Overview
  Transport Layer services & functions
  Internet Transport Layer
Multiplexing/ De-multiplexing
  Connectionless & connection-oriented
UDP Datagram Protocol
  UDP features
UDP Checksum
  Checksum calculation

## Slide 6: UDP checksum
sender:
treat contents of UDP segment (including header fields) as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment content
checksum value put into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  Not equal - error detected
  Equal - no error detected. But maybe errors nonetheless? More later ….
Goal: detect errors (i.e., flipped bits) in transmitted segment

## Slide 7: UDP Checksum (cont.)
How to compute checksum:
  Add all 16-bit words
  add any carry bits back in
  flip bits in sum to get checksum
Note: we’ll see same algorithm in detail when we look at IP
UDP checksum covers pseudo header of information from the IP header, the UDP header and the UDP data/payload
UDP checksum computation is optional for IPv4 (set to the value zero); mandatory when UDP runs over IPv6 (computation method changed).
Length
32 bits
4 bytes
Checksum
Source Port
Destination Port
相加所有16bit word(注意，UDP宽度32bit)
加进位
取反码
checksum组成
IP 头部
UDP 头部
UDP 数据

## Slide 8: UDP IPv4 Pseudo Header
UDP checksum based on pseudo header not real one
Protocol must = 17 (UDP)
Source and dest. addresses must match real IP header
UDP length must match value in UDP header
= 0
Proto. = 17
UDP Length
32 bits
4 bytes
Destination IP Address
Source IP Address
Notes: The pseudo header is used only for this calculation and is then discarded; it is not actually transmitted.

## Slide 9: Fields Used for Computing UDP Checksum
Pseudo Header
UDP Header
UDP data

## Slide 10: Internet checksum: an example
example: add two 16-bit integers
sum
checksum
Note: the overflow bit needs to be wrapped around.
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
1s complement to get the checksum
Notes: 1s complement to get the checksum: converting all the 0s to 1s and converting all the 1s to 0s

## Slide 11: Internet checksum: weak protection!
example: add two 16-bit integers
sum
checksum
1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
wraparound
1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
0 1
1 0
Even though numbers have changed (bit flips), no change in checksum!

## Slide 12: Summary: UDP
“no frills” protocol:
  segments may be lost, delivered out of order
  best effort service: “send and hope for the best”
UDP has its plusses:
  no setup/handshaking needed (no RTT incurred)
  can function when network service is compromised
  helps with reliability (checksum)
build additional functionality on top of UDP in application layer (e.g., HTTP/3)