## Slide 1: Network Layer I: roadmap
IPv4 & Addressing
  IPv4 datagram format
  IPv4 addressing
  IPv6

## Slide 2: IPv6: motivation
initial motivation: 32-bit IPv4 address space would be completely allocated
additional motivation:
  speed processing/forwarding: 40-byte fixed length header
  enable different network-layer treatment of “flows”
最初的动机:32位IPv4地址空间将被完全分配
额外的动机:．快速处理/转发:40字节固定长度的报头
    支持不同的网络层处理“流”

## Slide 3: IPv6
IPv6, first introduced in 1998
Address format
  128-bit addresses
  eight groups of four hexadecimal digits, separated by colons ‘:’
  Leading zeros in each group may be omitted and groups of zeros can be omitted using ‘::’
By Michel Bakni
128位地址
八组四个十六进制数字，用冒号':'隔开

## Slide 4: IPv6 datagram format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.” (concept of “flow” not well defined).
128-bit
IPv6 addresses
What’s missing (compared with IPv4):
no checksum (to speed processing at routers)
no fragmentation/reassembly
no options (the removal of options filed results in a fixed-length, 40-byte IP header)
(与IPv4相比)缺少什么:
没有校验和(以加快路由器的处理速度)
没有分裂/重新组装
无选项(删除选项字段会产生固定长度的40字节IP头)

## Slide 5: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
E隧道:IPv6数据报作为IPv4数据报的有效载荷在IPv4路由器之间被携带(“包中包”)

## Slide 6: IPv6: adoption
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
1 https://www.google.com/intl/en/ipv6/statistics.html

## Slide 7: Thank You!