## Slide 1: Network Layer II: roadmap
Dynamic Host Configuration Protocol (DHCP)
Network Address Translation (NAT)
Forwarding - what’s inside a router
  input ports, switching, output ports
  buffer management, scheduling

## Slide 2: Two key network-layer functions
network-layer functions:
forwarding: move packets from a router’s input link to appropriate router output link
analogy: taking a trip
forwarding: process of getting through single interchange
forwarding
routing
routing: process of planning trip from source to destination
routing: determine route taken by packets from source to destination
  routing algorithms
转发:将数据包从路由器的输入链路移动到相应的路由器输出链路
路由:确定数据包从源到目的所经过的路由

## Slide 3: Interplay between routing and forwarding
1
2
3
0111
value in arriving
packet’s header
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
routing algorithm determines
end-end path through network
forwarding table determines
local forwarding at this router
路由算法确定了通过网络的端到端路径
转发表决定了本路由器的本地转发

## Slide 4: Router architecture overview
high-level view of generic router architecture:
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
通用路由器架构的高级视图
路由管理控制平面(软件)
在毫秒时间帧内运行
转发数据平面(硬件)以纳秒的时间帧运行

## Slide 5: Input port functions
switch
fabric
line
termination
physical layer:
bit-level reception
link
layer
protocol
(receive)
link layer:
e.g., Ethernet
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
input port queuing: if datagrams arrive faster than forwarding rate into switch fabric
分散的切换:
使用报头字段值，使用输入端口内存中的转发表查找输出端口(“匹配+动作”)
基于目的的转发:只基于目的IP地址转发(传统)输入端口排队:如果数据报到达交换机的速度比转发速率快

## Slide 6: Destination-based forwarding
Q: but what happens if ranges don’t divide up so nicely?

## Slide 7: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address. (most specific match)
longest prefix match
Prefix
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001

## Slide 8: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 9: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 10: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 11: Switching fabrics
bus
memory
memory
interconnection
network
three major types of switching fabrics:
transfer packets from input ports to appropriate output ports
switching rate: rate at which packets can be transfer from inputs to outputs
将数据包从输入端口传输到相应的输出端口
交换速率:数据包从输入端传输到输出端的速率
三种主要类型的开关织物:

## Slide 12: Input port queuing
If switch fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
output port contention: only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
如果交换机结构比输入端口的组合速度慢—输入队列可能出现>排队．
由于输入缓冲区溢出导致排队延迟和丢失!
head -of- line (HOL)阻塞:在队列前面排队的数据报阻止队列中的其他数据报向前移动

## Slide 13: Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate. Drop policy: which datagrams to drop if no free buffers?
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R
当从fabric到达的数据报比链路传输速率快时，需要缓冲。
调度规程在以下方面进行选择的排队数据报传输
优先调度——谁能获得最好的性能，网络中立性

## Slide 14: Packet Scheduling: FCFS
packet scheduling: deciding which packet to send next on link
  first come, first served
  priority
  round robin
FCFS:
Packets transmitted in order of arrival
also known as: First-in-first-out (FIFO)
Simple implementation
No flow prioritization
No fairness, no isolation
Work-conserving scheduler
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R
分组调度:决定链路上下一个发送哪个分组
先到先得
轮循
按到达顺序传送的包
也被称为:先进先出(FIFO)
简单的实现
没有流优先级
没有公平，就没有孤立
Work-conserving调度器

## Slide 15: Scheduling policies: priority
Priority scheduling:
arriving traffic classified, into priority classes
  any header fields can be used for classification
high priority queue
low priority queue
arrivals
classify
departures
link
1
3
2
4
5
arrivals
departures
packet in service
send packet from highest priority queue that has buffered packets
  FCFS within priority class
1
3
4
2
5
1
3
2
4
5
优先级调度:
到达的交通按优先级分类
任何报头字段都可以用于分类
从已缓冲的最高优先级队列发送数据包
优先级中的FCFS

## Slide 16: Scheduling policies: round robin
Round Robin (RR) scheduling:
arriving traffic classified, queued by class
  any header fields can be used for classification
classify
arrivals
departures
link
R
server cyclically, repeatedly scans class queues, sending one complete packet from each class (if available) in turn
RR (Round Robin)调度:
对到达的流量进行分类，按类排队
任何报头字段都可以用于分类

## Slide 17: Thank You!