## Slide 1: Roadmap
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP

## Slide 2: Making routing scalable
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice
scale: hundreds of millions of routers:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network
不能在路由表中存储所有目的地!路由表交换将淹没链接!
行政自治权
每个网络管理员可能都想控制自己网络中的路由

## Slide 3: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems”(AS, a.k.a. “domains”, identified by an ASN number)
intra-AS (aka “intra-domain”): routing within same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other ASes
inter-AS (aka “inter-domain”): routing among ASes
gateways perform inter-domain routing (as well as intra-domain routing)
AS中的所有路由器必须运行相同的域内协议
不同AS中的路由器可以运行不同的域内路由协议
网关路由器:位于自身AS的“边缘”，与其他AS中的路由器有连接
将路由器聚合到区域中
自治系统
网关执行域间路由(以及域内路由)

## Slide 4: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations
intra-AS内路由确定AS内目的地的条目
inter-AS和intra-AS为外部目的地确定条目

## Slide 5: Inter-AS routing: a role in interdomain forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1, but which one?
1. 了解哪些目的地可以通过AS2到达，哪些通过AS3到达
2. 将这个可达性信息传播到AS1中的所有路由器

## Slide 6: Intra-AS routing: routing within an AS
most common intra-AS routing protocols:
RIP: Routing Information Protocol [RFC 1723]
  classic DV: DVs exchanged every 30 secs
EIGRP: Enhanced Interior Gateway Routing Protocol
  DV based
  formerly Cisco-proprietary for decades (became open in 2013 [RFC 7868])
OSPF: Open Shortest Path First [RFC 2328]
  link-state routing
  IS-IS protocol (ISO standard, not RFC standard) essentially same as OSPF
每30s广播更新信息
增强的内部网关路由协议

## Slide 7: OSPF (Open Shortest Path First) routing
“open”: publicly available
classic link-state
  each router floods OSPF link-state advertisements (directly over IP rather than using TCP/UDP) to all other routers in entire AS
  multiple link cost metrics possible: bandwidth, delay
  each router has full topology, uses Dijkstra’s algorithm to compute forwarding table
security: all OSPF messages authenticated (to prevent malicious intrusion)
每个路由器将OSPF链路状态广告(直接通过IP而不是使用TCP/UDP)发送到整个AS中的所有其他路由器
每个路由器都有完整的拓扑结构，采用Dijkstra算法计算转发表
安全性:所有OSPF消息都经过验证(防止恶意入侵)

## Slide 8: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations
area border routers: “summarize” distances to destinations in own area, advertise in backbone
area 1
area 2
area 3
backbone
internal
routers
backbone router: runs OSPF limited to backbone
boundary router: connects to other ASes
local routers:
flood LS in area only
compute routing within area
forward packets to outside via area border router
链接状态广告只在区域或主干泛滥
每个节点都有详细的area拓扑;只知道去其他目的地的方向