## Slide 1: Internet Traffic Monitoring and Analysis: Wireshark Tutorial
Kevin Curran

## Slide 2: What is Wireshark?
The Network Protocol Analyzer
  Open-Source (GNU Public License)
  Multi-platform (Windows, Linux, OS X, Solaris, FreeBSD, NetBSD, and others)
  Easily extensible
  Large development group
Previously Named “Ethereal”
Features
  Deep inspection of thousands of protocols
  Live capture and offline analysis
  Standard three-pane packet browser
  Captured network data can be browsed via a GUI, or via the TTY-mode TShark utility
  The most powerful display filters in the industry
  Rich VoIP analysis
  Live data can be read from Ethernet, IEEE 802.11, PPP/HDLC, ATM, Bluetooth, USB, Token Ring, Frame Relay, FDDI, and others
  Coloring rules can be applied to the packet list for quick, intuitive analysis
  Output can be exported to XML, PostScript®, CSV, or plain text

## Slide 3: What is Wireshark?
What we can do:
  Capture network traffic
  Decode packet protocols using dissectors
  Define filters – capture and display
  Watch smart statistics
  Analyze problems
  Interactively browse that traffic
Some examples people use Wireshark for:
  Network administrators: troubleshoot network problems
  Network security engineers: examine security problems
  Developers: debug protocol implementations
  People: learn network protocol internals

## Slide 4: Interfaces
Packet
List
Packet
Details
Packet
Bytes

## Slide 5: Capturing Packets (1/3)

## Slide 6: Capturing Packets (2/3)
Buffer size – in order not to fill your laptop disk
Capture all packets on the network
Capture filter
Capture in multiple files
When to automatically stop the capture
Display options
Name resolution options

## Slide 7: Capturing Packets (3/3)
Example (W-LAN):
Received Signal Strength Indication (RSSI) and Link speed (BW)

## Slide 8: Analyzing Packets (1/9)
Ethernet Frame Example

## Slide 9: Analyzing Packets (2/9)
IP Packet Example

## Slide 10: Analyzing Packets (3/9)
TCP Packet Example

## Slide 11: Analyzing Packets (4/9)
TCP 3-way Handshake
SYN
SYN, ACK
ACK

## Slide 12: Analyzing Packets (5/9)
Flow Graph
  Giving us a graphical flow, for better understanding of what we see

## Slide 13: Analyzing Packets (6/9)
Flow Graph

## Slide 14: Analyzing Packets (7/9)
Filtering Specific TCP Stream

## Slide 15: Analyzing Packets (8/9)
Filtering Specific TCP Stream

## Slide 16: Analyzing Packets (9/9)
RTP Stream Analysis
Stable stream BW

## Slide 17: Filtering Packets (1/4)
Applying Filter when Capturing Packets
Capture  Interfaces  Options:

## Slide 18: Filtering Packets (2/4)
Applying Filter when Analyzing Packets

## Slide 19: Filtering Packets (3/4)
  Capture only traffic to or from IP address 172.18.5.4
    host 172.18.5.4
  Capture traffic to or from a range of IP addresses
    net 192.168.0.0/24
    net 192.168.0.0 mask 255.255.255.0
  Capture traffic from a range of IP addresses
    src net 192.168.0.0/24
    src net 192.168.0.0 mask 255.255.255.0
  Capture traffic to a range of IP addresses
    dst net 192.168.0.0/24
    dst net 192.168.0.0 mask 255.255.255.0
  Capture only DNS (port 53) traffic
    port 53
  Capture non-HTTP and non-SMTP traffic on your server
    host www.example.com and not (port 80 or port 25)
    host www.example.com and not port 80 and not port 25
  Capture except all ARP and DNS traffic
    port not 53 and not arp
  Capture traffic within a range of ports
    (tcp[2:2] > 1500 and tcp[2:2] < 1550) or (tcp[4:2] > 1500 and tcp[4:2] < 1550)
    tcp portrange 1501-1549
  Capture only Ethernet type EAPOL
    ether proto 0x888e
  Capture only IP traffic
    (the shortest filter, but sometimes very useful to get rid of lower layer protocols like ARP and STP)
    ip
  Capture only unicast traffic
    (useful to get rid of noise on the network if you only want to see traffic to and from your machine, not, for example, broadcast and multicast announcements)
    not broadcast and not multicast

## Slide 20: Saving and Manipulating Packets (1/3)
Save only displayed packets

## Slide 21: Saving and Manipulating Packets (2/3)
Export to CSV file
Exported CSV File

## Slide 22: Packet Statistics
Protocol Hierarchy
Conversation
  Traffic between two specific endpoints

## Slide 23: Packet Statistics
I/O Graph
Configurable Options
  I/O Graphs
    Graph 1-5: enable the specific graph 1-5 (graph 1 by default)
    Filter: a display filter for this graph (only the packets that pass this filter will be taken into account for this graph)
    Style: the style of the graph (Line/Impulse/FBar/Dot)
  X Axis
    Tick interval: an interval in x direction lasts (10/1 minutes or 10/1/0.1/0.01/0.001 seconds)
    Pixels per tick: use 10/5/2/1 pixels per tick interval
    View as time of day: option to view x direction labels as time of day instead of seconds or minutes since beginning of capture
  Y Axis
    Unit: the unit for the y direction (Packets/Tick, Bytes/Tick, Bits/Tick, Advanced...)
    Scale: the scale for the y unit (Logarithmic,Auto,10,20,50,100,200,...)

## Slide 24: Packet Statistics
TCP Stream Graph
Round-Trip Time Graph
RTT Vs. Sequence numbers gives us the time that take to Ack every packet.
In case of variations, it can cause DUPACKs and even Retransmissions
Usually will happen on communications lines:
  Over the Internet
  Over cellular networks

## Slide 25: Packet Statistics
Time / Sequence Graph
Seq No [B]
Time [Sec]
Time / Sequence represents how sequence numbers advances with time
In a good connection (like in the example), the line will be linear
The angle of the line indicates the speed of the connection. In this example – fast connection
Seq No [B]
Time [Sec]
In this case, we see a non-contiguous graph
Can be due to:
  Severe packet loss
  Server response (processing) time
Time / Sequence Graph
Notes: Time / Sequence representes how sequence numbers advances with time
In a good connection (like in the example), the line will be linear
The angle of the line indicates the speed of the connection. In this example – fast connection

## Slide 26: Colorizing Specific Packets (1/4)
Packet Colorization
  Colorize packets according to a filter
  Allow to emphasize the packets interested in
  A lot of Coloring Rule examples at the Wireshark Wiki Coloring Rules page at http://wiki.wireshark.org/ColoringRules
We want to watch a specific protocol through out the capture file

## Slide 27: Colorizing Specific Packets (2/4)
Notes: There are two types of coloring rules in Wireshark. Temporary ones that are only used until you quit the program. And permanent ones that will be saved to a preference file so that they are available on a next session.
Temporary coloring rules can be added by selecting a packet and pressing the <ctrl> key together with one of the number keys. This will create a coloring rule based on the currently selected conversation. It will try to create a conversation filter based on TCP first, then UDP, then IP and at last Ethernet. Temporary filters can also be created by selecting the "Colorize with Filter > Color X" menu items when rightclicking in the packet-detail pane.

## Slide 28: Colorizing Specific Packets (3/4)

## Slide 29: Colorizing Specific Packets (4/4)
TLS Connection Establishment

## Slide 30: References
Wireshark Website
  http://www.wireshark.org
Wireshark Documentation
  http://www.wireshark.org/docs/
Wireshark Wiki
  http://wiki.wireshark.org
Network analysis Using Wireshark Cookbook
  http://www.amazon.com/Network-Analysis-Using-Wireshark-Cookbook/dp/1849517649