## Slide 1: CNSCC.203 Computer Networks Revision
Muhammad Azhar Iqbal
azhar.iqbal@lancaster.ac.uk
Credit goes to Dr. Matt Broadbent and Dr. Vasileios Giotsas at SCC for designing module SCC.203.

## Slide 2: Week 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Chapter 1.1-1.3

## Slide 3: Internet structure
The Internet is fundamentally made up of core and edge networks
An edge network can be defined as a network which connects end systems to the edge router
A core network connects these edge networks together using packet switches and links
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 4: Access networks and physical media
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Q: How to connect end systems to edge router?
residential access networks
institutional access networks (school, company)
mobile access networks (WiFi, 4G/5G)

## Slide 5: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
  Store and forward: entire packet must arrive at router before it can be transmitted on next link
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 6: Alternative to packet switching: circuit switching
end-to-end resources allocated to, reserved for “call” between source and destination
establish a connection between source and destination before transmission
  connection: called “circuit” (virtual)
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
commonly used in traditional telephone networks
4 virtual “circuits”
2nd circuit
1st circuit
A simple circuit-switched network:
in diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.

## Slide 7: Internet structure: a “network of networks”
Hosts connect to Internet via access Internet Service Providers (ISPs)
    residential, enterprise (company, university, commercial) ISPs
Access ISPs in turn must be interconnected
    so that any two hosts can send packets to each other
Resulting network of networks is very complex
    evolution was driven by economics and national policies

## Slide 8: Internet structure: a “network of networks”
Tier 1 ISP
Tier 1 ISP
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
IXP
IXP
IXP
At “center”: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider networks (e.g., Google, Facebook): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
Google

## Slide 9: Week 2: roadmap
Performance: delay, loss, throughput
Protocol layers, service models
Chapter 1.4-1.5

## Slide 10: Types of delay
4 main types of delay present in every network:
    Processing delay
    Queuing delay
    Transmission delay
    Propagation delay
Together, these are known as Nodal delay

## Slide 11: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dnodal: nodal delay
Total of all previously mentioned types of delay
Measured per node (each device in a network)

## Slide 12: End-to-end delay
Definition: end-to-end delay is the total of all nodal delay from source to destination
  Include a sequence of intermediate nodes on the way to the destination
Varies over time as the sources of delay increase and decrease
Delay components: transmission delay dtrans, propagation delay dprop, processing delay dproc and queuing delay dqueue
Round-trip time (RTT): end-to-end delay measured in both directions
  from source to destination and then back again
  Doesn’t necessarily have to be the same path/route

## Slide 13: Packet loss overview
Packet Loss occurs when a node drops or discards a packet
This means that the packet does not reach its destination
Packet loss can occur due to arriving to a full buffer or other reasons including hardware/software failure, unguided radio etc.
Packet Loss reduces the useable throughput of a device, as the number of useful bits sent is less
For reliable protocols, packet loss will cause retransmission
  This introduces additional latency, as the packet has to make the full journey again, regardless of where it was lost

## Slide 14: Throughput
Rs < Rc What is average end-to-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-to-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec
Rc
Rs
Average end-to-end throughput: min(Rc , Rs)

## Slide 15: Internet protocol stack
application: supporting network applications
  IMAP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), DOCSIS
physical: move bits from one node to the next
application
transport
network
link
physical

## Slide 16: Application layer: overview
Principles of network applications
Socket programming with UDP and TCP
Application architectures
Web and HTTP
The Domain Name System DNS
E-mail, SMTP, POP3, IMAP
Chapter 2.1- 2.7

## Slide 17: HTTP overview
HTTP: hypertext transfer protocol
Web’s application layer protocol
client/server model:
  client: browser that requests, receives, (using HTTP protocol) and “displays” Web objects
  server: Web server sends (using HTTP protocol) objects in response to requests
“stateless” server maintains no information about past client requests
Uses TCP underneath
PC running
Firefox browser
server running
Apache Web
server
iPhone running
Safari browser
HTTP request
HTTP response
HTTP request
HTTP response

## Slide 18: HTTP connections: two types
Non-persistent HTTP
at most one object sent over TCP connection
  TCP connection then closed
downloading multiple objects required multiple connections
Persistent HTTP (Keep-alive)
multiple objects can be sent over single TCP connection between client, and that server

## Slide 19: Web caches (proxy servers)
user configures browser to point to a Web cache
browser sends all HTTP requests to cache
  if object in cache: cache returns object to client
  else cache requests object from origin server, caches received object, then returns object to client
Goal: satisfy client request without involving origin server
client
proxy
server
client
HTTP request
HTTP response
HTTP request
HTTP request
origin
server
origin
server
HTTP response
HTTP response

## Slide 20: Web caches (proxy servers)
Web cache acts as both client and server
  server for original requesting client
  client to origin server
Why Web caching?
reduce response time for client request
  cache is closer to client
reduce traffic on an institution’s access link
Internet is dense with caches
  enables “poor” content providers to more effectively deliver content

## Slide 21: DNS: Domain Name System
people: many identifiers:
  name, passport #, ID number
Internet hosts, routers:
  IP address (32 bit) - used for addressing datagrams
  “name”, e.g., www.yahoo.com- used by humans
Q: how to map between IP address and name, and vice versa ?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, name servers communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  Runs over UDP and uses port 53
  complexity at network’s “edge”

## Slide 22: DNS name resolution: iterative query
Example: host at engineering.nyu.edu wants IP address for gaia.cs.umass.edu
Iterative query:
contacted server replies with name of server to contact
Recursive query:
puts burden of name resolution on contacted name server
In reality, a mixture of both types
requesting host at
engineering.nyu.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.nyu.edu
1
2
3
4
5
6
authoritative DNS server
dns.umass.edu
7
8
TLD DNS server

## Slide 23: Caching, Updating DNS Records
once (any) name server learns mapping, it caches mapping
  cached entries timeout (disappear) after some time (TTL)
  TLD servers typically cached in local name servers
    thus root name servers not often visited
cached entries may be out-of-date (best-effort name-to-address translation!)
  if name host changes IP address, may not be known Internet-wide until all TTLs expire!

## Slide 24: Email
sender’s e-mail
server
SMTP
SMTP
e-mail access
protocol
receiver’s e-mail
server
(e.g., POP3, IMAP, HTTP)
user
agent
user
agent
SMTP: used to transfer mail from the sender’s user agent to the sender’s mail server and used to transfer mail from the sender’s mail server to the recipient’s mail server
mail access protocol: retrieval from mail server
  POP3 is very basic, with limited functionality
  IMAP allows folder organization, and messages stay on the server
  HTTP is used for the web-based email
Alice
Bob