## Slide 1: Link Layer and LANs - Roadmap
introduction
error detection, correction
multiple access protocols
LANs
  addressing, ARP
  Ethernet
  switches
Chapter 6.1- 6.4.3

## Slide 2: Parity checking
single bit parity:
detect single bit errors
0111000110101011
1
parity
bit
d data bits
two-dimensional bit parity:
detect and correct single bit errors
14% overhead
d1,1
d2,1
di,1
. . .
d1,j+1
d2,j+1
di,j+1
. . .
. . .
d1,j
d2,j
di,j
. . .
di+1,1
di+1,j+1
di+1,j
. . .
. . .
. . .
. . .
row parity
column
parity
0 1 1 1 0 1
1 0 1 0 1 1
1 1 1 1 0 0
1 0 1 0 1 0
no errors:
0 1 1 1 0 1
1 0 1 0 1 1
1 0 1 1 0 0
1 0 1 0 1 0
parity
error
parity
error
detected
and
correctable
single-bit
error:
Even parity: add an extra bit called parity bit to keep the number of 1’s even
Detects 1-bit errors and some 2-bit errors
Not reliable against bursty errors

## Slide 3: Cyclic Redundancy Check (CRC)
CRC:
  Sender and receiver agree on a generator G of r+1 bits
    e.g., generator polynomial: G() =
  Append r bits of 0 at the end of data D
  Divide the padded data by G using modulo-2 arithmetic
  The remainder is the CRC bits which will be appended to the data bits and transmitted
very powerful error detection technique
  Each of the CRC standards can detect burst errors of fewer than r+1 bits, sometimes even larger bursts of errors
  Data-link layer protocols usually implemented in hardware, therefore can afford more computationally intensive error detection

## Slide 4: Cyclic Redundancy Check (CRC): example
1 0 0 1
1 0 1 0
1 0 1
0 0 0
1 0 0 1
1 0 0 1
1 0 0 1
0 0 0
1 1 0
1 1 0 0
1 0 1 0
0 1 1
0 1 1
D
R
1 0 0 1
G
0 0 0
1 0 1 1 1 0
2r
*
1
0
1
D = 101110
G = 1001
Generator polynomial:
Since G is 4 bits long, the CRC bits are 3 bits.
Append 3 bits of 0 at the end of data D
Divide the padded data by G using modulo-2 arithmetic
Finally, the 3-bit long remainder is the CRC bits which will be appended to the data bits at the sender side before the transmission

## Slide 5: Random access protocols
when node has packet to send
  transmit at full channel data rate R.
  no a priori coordination among nodes
two or more transmitting nodes: “collision”
random access MAC protocol specifies:
  how to detect collisions
  how to recover from collisions (e.g., via delayed retransmissions)
examples of random access MAC protocols:
  ALOHA, slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA

## Slide 6: Pure ALOHA
unslotted Aloha: simple, no synchronization
  when frame first arrives: transmit immediately
  Receivers ACK all received packets
  No ACK = collision, wait a random time then retransmit
In the following example scenario,
  frame sent at t0 collides with the other frame sent in [t0-1,t0]
t0 + 1
t0 - 1
t0
will overlap
with end of
i’s frame
will overlap
with start of
i’s frame

## Slide 7: Slotted ALOHA
assumptions:
all frames same size
time divided into equal size slots (time to transmit 1 frame)
nodes start to transmit only slot beginning
nodes are synchronized
if 2 or more nodes transmit in slot, all nodes detect collision before the slot ends
operation:
when node obtains fresh frame, transmits in next slot
  if no collision: node can send new frame in next slot if it has one
  if collision: node retransmits frame in each subsequent slot with probability p until success (like tossing a biased coin)

## Slide 8: Slotted ALOHA: performance
efficiency: long-run fraction of successful slots (many nodes, all with many frames to send)
suppose: N nodes with many frames to send, each transmits in slot with probability p
  prob that a given node has success in a slot = p(1-p)N-1
  For all N nodes, the efficiency of slotted ALOHA = Np(1-p)N-1
  max efficiency: find p* that maximizes Np(1-p)N-1
  for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives:
max efficiency = 1/e = .37
at best: channel is used for useful transmissions for 37% of time!

## Slide 9: CSMA/CD
Carrier sense multiple access with collision detection
Algorithm
  Listen to the channel
  If channel is busy, wait until idle
    Sending would cause a collision and waste time
  Send a frame and sense for collision
  If no collision, then frame has been delivered
  If collision, abort immediately (stops transmission)
    Why keep sending if the frame is already corrupted?
  Perform exponential backoff then retransmit

## Slide 10: Exponential Backoff
When a sender detects a collision, send “jam signal”
  Make sure all hosts are aware of collision
  Jam signal is 32 bits long (plus header overhead)
Exponential backoff
  Select k ∈ [0, 2n – 1], where n = number of collisions
  Wait k * the amount of time required to send 512 bits (e.g., k * 51.2µs for 100 Mbps Ethernet) before retransmission
  n is capped at 10, frame dropped after 16 collisions
  The size of the sets from which k is chosen grows exponentially with the number of collisions – exponential backoff

## Slide 11: CSMA/CA
Carrier Sense Multiple Access / Collision Avoidance
Like CSMA/CD, CSMA/CA it is also operated in the medium access control layer.
Unlike CSMA/CD (that is effective after a collision), CSMA / CA is effective before a collision
Algorithm
  prior to transmitting, a node first listens to the shared medium (such as listening for wireless signals in a wireless network) to determine whether another node is transmitting or not.
  if another node was heard, wait for a period of time (usually random) for the node to stop transmitting before listening again for a free communications channel.
  if the medium was identified as being clear then it can send the frame in its entirety.

## Slide 12: CSMA/CD vs CSMA/CA
S.NO | CSMA/CD | CSMA/CA
1. | CSMA / CD is effective after a collision. | Whereas CSMA / CA is effective before a collision.
2. | CSMA / CD is used in wired networks. | Whereas CSMA / CA is commonly used in wireless networks.
3. | It only reduces the recovery time. | Whereas CSMA/ CA minimizes the possibility of collision.

## Slide 13: ARP: address resolution protocol
ARP table: each IP node (host, router) on LAN has table
Question: how to determine interface’s MAC address, knowing its IP address?
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.78
137.196.7.14
137.196.7.88
137.196.7.23
ARP
ARP
ARP
ARP
  IP/MAC address mappings for some LAN nodes:
< IP address; MAC address; TTL>
  TTL (Time To Live): time after which address mapping will be forgotten (typically 20 min)

## Slide 14: Thank You!